## Slide 1
Range processing

## Slide 2: Range Processing Block Diagram
Input is from ADC, assuming data is in 16-bit I/Q format, and stored in memory in imag/real order.
1D windowing is 16-bit I/Q in and 16-bit I/Q or SP float out, depending on 1D FFT type. The function also scale the signal depending on number of ADC bits.
1D FFT is either fixed-point DSP_fft16x16_imre (note the issue on DC, but does not affect results), or floating-point DSPF_sp_fftSPxSP.
Option to include 2D windowing inside range processing.
  If not included, range processing output format must be the same as 1D FFT output format.
  If included, processing output format can be either 16-bit I/Q fixed-point, or single precision floating point. Format conversion is done by 2D windowing function.
Memory used
  nSamplesPerChirp/2 * sizeof(uint16_t) bytes for 1D window function
  numChirpsPerFrame/2 * sizeof(uint16_t) bytes for 2D window function if 2D windowing is included
  2 * fft1DSize * sizeof (int16_t) bytes for DSP_fft16x16_imre twiddle factors, or 2 * fft1DSize * sizeof (float) bytes for DSPF_sp_fftSPxS twiddle factors

## Slide 3: Range Processing Benchmarks (C66x)
FFT size | FFT type | 2D Win included | Output Format | cycles
64 | 16x16 | no | 16x16 | 585
128 | 16x16 | no | 16x16 | 1177
256 | 16x16 | no | 16x16 | 1612
512 | 16x16 | no | 16x16 | 3890
1024 | 16x16 | no | 16x16 | 6744
2048 | 16x16 | no | 16x16 | 16873
4096 | 16x16 | no | 16x16 | 31806
64 | 16x16 | yes | 16x16 | 735
128 | 16x16 | yes | 16x16 | 1422
256 | 16x16 | yes | 16x16 | 2013
512 | 16x16 | yes | 16x16 | 4913
1024 | 16x16 | yes | 16x16 | 8385
2048 | 16x16 | yes | 16x16 | 19863
4096 | 16x16 | yes | 16x16 | 38691
64 | 16x16 | yes | float | 672
128 | 16x16 | yes | float | 1082
256 | 16x16 | yes | float | 1929
512 | 16x16 | yes | float | 4551
1024 | 16x16 | yes | float | 7678
2048 | 16x16 | yes | float | 18310
4096 | 16x16 | yes | float | 35419
64 | float | no | float | 1192
128 | float | no | float | 2228
256 | float | no | float | 4121
512 | float | no | float | 8715
1024 | float | no | float | 16364
2048 | float | no | float | 38140
4096 | float | no | float | 80308
64 | float | yes | float | 1354
128 | float | yes | float | 2518
256 | float | yes | float | 4659
512 | float | yes | float | 9728
1024 | float | yes | float | 18452
2048 | float | yes | float | 41928
4096 | float | yes | float | 87604

## Slide 4: Range Processing Benchmarks (C674x)
FFT size | FFT type | 2D Win included | Output Format | cycles
64 | 16x16 | no | 16x16 | 876
128 | 16x16 | no | 16x16 | 1539
256 | 16x16 | no | 16x16 | 2351
512 | 16x16 | no | 16x16 | 5066
1024 | 16x16 | no | 16x16 | 12882
2048 | 16x16 | no | 16x16 | 31399
4096 | 16x16 | no | 16x16 | 63491
64 | 16x16 | yes | 16x16 | 1130
128 | 16x16 | yes | 16x16 | 1907
256 | 16x16 | yes | 16x16 | 2887
512 | 16x16 | yes | 16x16 | 6102
1024 | 16x16 | yes | 16x16 | 12914
2048 | 16x16 | yes | 16x16 | 29333
4096 | 16x16 | yes | 16x16 | 60383
64 | 16x16 | yes | float | 1104
128 | 16x16 | yes | float | 1915
256 | 16x16 | yes | float | 2871
512 | 16x16 | yes | float | 5856
1024 | 16x16 | yes | float | 12498
2048 | 16x16 | yes | float | 28117
4096 | 16x16 | yes | float | 60167
64 | float | no | float | 1568
128 | float | no | float | 2996
256 | float | no | float | 5627
512 | float | no | float | 12163
1024 | float | no | float | 24084
2048 | float | no | float | 60793
4096 | float | no | float | 130840
64 | float | yes | float | 1926
128 | float | yes | float | 3529
256 | float | yes | float | 6367
512 | float | yes | float | 13385
1024 | float | yes | float | 26525
2048 | float | yes | float | 62534
4096 | float | yes | float | 131452